SECTION I - PRODUCT IDENTIFICATION

Chemical Name:	Phosphoric Acid

Product Name	IG-62

CAS Number	7664-38-2

Manufacturer's Name:	Encee Chemical Sales

Address:			P.O. Box 39

New Bern, NC  28560

Emergency Telephone Numbers:	Manufacturer (252) 633-5868

CHEMTREC: (800) 424-9300 (24 hr)

SECTION II - HAZARDOUS INGREDIENTS/ IDENTITY INFORMATION

Material or Component	Percentage		Hazard Data

Phosphoric Acid		62%			Oral-Rats LD50  	1530 mg/kg

SECTION III- PHYSICAL/CHEMICAL CHARACTERISTICS

Boiling Point (oF)	260	Specific Gravity (H2O)=1	1.51

Melting Point	N/A	Solubility in Water	Complete

Evaporation Rate  (Butyl Acetate=1)   N/A	Percent Volatiles by Volume	N/A

Vapor Pressure (75oF)	< 10 mm Hg	Appearance and Odor	Green Liquid

Acrid Odor   Vapor Density (Air=1)	N/A

SECTION IV - FIRE AND EXPLOSION HAZARD

Flash Point	Not Combustible

Autoignition Temperature	N/A

Flammable Air Limits, % by Volume	N/A

Extinguishing Media	N/A

Special Fire Fighting Procedures	Use Self Contained Breathing Apparatus

Use Full Acid Resistant Clothing

Unusual Fire and Explosion Hazards	Toxic and Irritating Phosphorous Oxides May Form

Contact with Metals May Cause Formation of Flammable and Explosive Hydrogen Gas

SECTION V - REACTIVITY DATA

Stability	Stable

Conditions to Avoid	High Temperature -- May Cause Release of Highly Irritating Phosphorous Oxides

Incompatibility	Strong Bases

Hazardous Decomposition Products	Phosphoric Acid Mist or Fumes, and Phosphorous Oxides

SECTION IV - HEALTH HAZARD INFORMATION

Toxicity/Health Hazard Data	Oral - See Section II

Skin - Unknown

Eye -  Unknown

Air -  TLV (ACGIH)  1 /mg/m3 for eight hour weighted average;

PEL (OSHA) 1/mg /m3

Routes of Exposure	Ingestion - nausea, vomiting, stomach pain, diarrhea and shock,  can be fatal

Skin Contact - irritant

Eye - Severe irritation, permanent damage or blindness

Inhalation - Irritation of nose, throat, and respiratory tract

Effects of Acute Overexposure	Large amounts of oral dosage can be serious or fatal see ingestion under routes of exposure.

Effects of Chronic Overexposure	See effects of acute exposure.

Emergency and First Aid Procedures	Ingestion -  If patient is conscious give large amounts of water and induce vomiting.  Seek medical attention

Skin Contact - Flush with water.  Remove Contaminated Clothing.

Inhalation - Remove to Fresh Air.  If discomfort continues seek medical attention.

Eye Contact - Wash with water for at least 15 minutes, including under the eyelid.  Seek medical attention.

Notes to Physician	Advise of Phosphoric Acid Exposure

| SECTION VII - PRECAUTIONS FOR SAFE HANDLING/SPILL-LEAK PROCEDURES |
| --- |
| Procedure for Leak or Spill | Do not allow anyone to come in contact with spilled material. Contain by diking. Prevent large quantities form entering waterways or from contact with vegetation. |
| Neutralizing Chemicals | Soda Ash or Lime |
| Waste Disposal Method | If uncontaminated, recover and reuse. Consult Local, State, Federal Regulations. |
| Precautions for Storage and Handling | Store in a well ventilated location away from fire hazards. Use a container suitable for phosphoric acid. Do not use metals which react with acids including 304 stainless steels as the acid will cause the formation of hydrogen gas. |
| Other Precautions | Use suitable containers. Do not take internally. Avoid eye and skin contact. Avoid inhaling mist. |

| SECTION VIII - PROTECTION/CONTROL MEASURES |
| --- |
| Ventilation | Maintain adequate ventilation. See TLV Section IV. |
| Eyes | Wear splash goggles with a face shield. |
| Skin | Wear impervious acid resistant clothing. |
| Respiratory Equipment | NIOSH/OSHA approved dust or mist respirator when the phosphoric acid mist exposure will exceed the OSHA standard of 1 /mg/m3 |
| Other Equipment | A safety shower and eye wash station shall be available where phosphoric acid is used. |

| SECTION IX - SUPPLIER NOTIFICATION |
| --- |
| Shipping Name | Phosphoric Acid |
| Hazard Label | Corrosive |
| Freight Classification | Chemicals, Liquid |
| Transportation Guidelines | Use approved shipping containers. |

| SECTION X - REFERENCES |
| --- |
| Date Prepared | June, 1991 |